SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION		Clanton Park - 2 Play Spaces, Junior East of Path, Senior West of Path 	         							Ward 8

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01TTW3004P |  | -pinch & crush points | -remove and replace |  |  |  | -site replacement |
| Teeter Totter |  |  |  |  |  |  |  |
| PLG01SSM2511P |  | -improper seats | -replace |  |  |  |  |
| Swing Set |  | -S-hooks | -replace |  |  |  |  |
| PLG02SSM2511P |  | -protrusions | -adjust bearings |  |  |  |  |
| Swing Set |  | -improper spacing | -remove one belt |  |  |  |  |
| PLG03SSM2511P |  | -improper spacing | -remove one swing |  |  |  |  |
| Swing Set |  | -protrusions | -adjust bearings |  |  |  |  |
| PLG04JRW2511P |  | -entanglement on both slides | -caulk gaps |  |  |  |  |
| Jr. Cr. Structure |  | -barriers at sides, openings, stair access | -lower change stair rails, slide hoods |  |  |  |  |
|  |  | -ladder pole climber too far away, high | -change to vertical rung attached |  |  |  |  |
|  |  | -elevated surfaces | -cap |  |  |  |  |
|  |  | -play table too close to climber | -remove |  |  |  |  |
| PLG05SRW2511P |  | -track ride attached, no safety zone | -remove or relocate |  |  |  | -pending |
| Sr. Cr. Structure |  | -entanglement at senior slide | -caulk gap |  |  |  |  |
|  |  | -access ladder away from platform | -replace three |  |  |  |  |
|  |  | -curved bridge no barriers | -add quarter inch lexan |  |  |  |  |
| PLG05SRW2511P |  | -play surfaces | -add cap |  |  |  |  |
| Con’t |  | -barriers (slide & openings too low) | -change or retrofit |  |  |  |  |
|  |  | -log chain climber | -change to rungs, install at 75º |  |  |  |  |
|  |  | -fire pole too close | -move out |  |  |  |  |
|  |  | -horizontal ladder rungs too far | -remove and cap |  |  |  |  |
| Base Material |  | -compacted | -rototill |  |  |  |  |
|  |  |  | -excavate |  |  |  |  |
| Total |  |  |  | 0 | 0 | 0 |  |

File Name: K:\PLAY\NORTH\WARD-8\CLANTON