SITE SPECIFIC RECOMMENDATIONS

EAST 	REGION:	Central District

LOCATION		Stephen Leacock														Ward 14

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM - 126 |  | -too many swings | -remove one baby, adjust spacing |  | 1 |  |  |
| 2 Belt 2 Baby |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -hanger bearings | -replace | 80 | 1 |  |  |
|  |  | -improper baby seat | -replace | 50 | 1 |  |  |
| PLG02SST - 126 |  | -barriers | -pickets over 30” | 100 | 2 |  |  |
| Int. Str. Slide |  | -handrail | -replace |  |  |  |  |
| PLG03RCM - 126 |  | -nil |  |  |  |  |  |
| Rainbow Climber |  |  |  |  |  |  |  |
| PLG04INM - 126 |  | -barriers | -pickets over 30” | 100 | 2 |  |  |
| Int. Cr. Structure |  | -entanglement | -weld |  | 1 |  |  |
|  |  | -entrapments |  |  |  |  |  |
|  |  | -bolts too lone | -correct |  | 1 |  |  |
|  |  | -steering wheel | -replace | 60 | 1 |  |  |
|  |  | -fireman pole too low | -raise |  | 1 |  |  |
| Base Material |  |  | -rototill, add base material 50T |  | 8 | 750 |  |
|  |  |  | -excavate |  | 8 | 1000 |  |
| TOTAL COST |  |  |  | 400 | 28 | 1750 |  |

File Name: K:\PLAY\SCARB\WARD-14\LEACOCK.WPD