SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	East District

LOCATION 		Linkwood Lane Park														Ward 11

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG02SSM5535P |  | -non sufficient safety zone | -relocate | 100 | 12 |  | -add spring toys or Teeter |
| 2 Belt |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -elevated surfaces | -cap | 10 | 1 |  |  |
|  |  | -protrusions | -remove | 10 | 1 |  |  |
| PLG03SSM5535P |  | -non sufficient safety zone | -relocate | 100 | 12 |  |  |
| 2 Baby |  | -seats & S-hooks | -replace | 140 | 1 |  |  |
|  |  | -elevated surfaces | -cap | 10 | 2 |  |  |
|  |  | -protrusions | -remove |  | 1 |  |  |
| PLG04JRW5535P |  | -no pickets on platform | -picket openings over 15” | 300 | 8 |  |  |
| Jr. Cr. Structure |  | -log chain climbers pinch points | -retrofit | 300 | 16 |  |  |
|  |  | -wood chain climber pinch points | -retrofit | 80 | 8 |  |  |
|  |  | -half tube slide - no barriers | -retrofit | 400 | 3 |  |  |
|  |  | -fire pole lower barrier to be moved | -move |  | 1 |  |  |
|  |  | -elevated surface | -rout |  | 3 |  |  |
|  |  | -rope climber rope inappropriate | -change, retrofit | 200 | 4 |  |  |
|  |  | -access hand holds | -install | 100 | 4 |  |  |
| PLG05SRW5535P |  | -no pickets on platform | -picket openings over 15” | 300 | 8 |  |  |
| Sr. Cr. Structure |  | -slide sidewalls, entanglement | -replace with tube slide | 1500 | 12 |  |  |
|  |  | -access hand holds | -install | 40 | 6 |  |  |
|  |  | -play ledge too high | -lower |  | 1 |  |  |
| PLG05SRW5535P |  | -tube slide entanglement | -in fill | 20 | 2 |  |  |
|  |  | -decking lifting | -screw down | 20 | 4 |  |  |
|  |  | -track ride interferes with other items | -remove |  | 4 |  |  |
| Base Material |  | -compacted | -rototill and top up 16oT |  | 8 | 2400 |  |
|  |  |  | -excavate |  | 8 | 2500 |  |
| Total |  |  |  | 3640 | 131 | 4900 |  |

File Name: K:\PLAY\NORTH\WARD-11\LINKWOOD