SITE SPECIFIC RECOMMENDATIONS

EAST 	REGION:	North District

LOCATION		Whitehaven West														Ward 18

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM - 114W |  | -improper spacing | -remove two swings |  | 1 |  |  |
| 4 Belt |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -chipped paint | -repaint | 50 | 2 |  |  |
|  |  | -non sufficient safety zone |  |  |  |  |  |
| PLG02SSC - 114W |  | -climber | -remove |  | 2 |  |  |
| Climber Swings |  | -trapeze | -remove |  | 2 |  |  |
|  |  | -swings | -add 2 baby, 2 belt | 400 | 2 |  |  |
|  |  | -chipped paint | -repaint | 50 | 2 |  |  |
|  |  | -non sufficient safety zone |  |  |  |  |  |
| PLG03TTM - 114W |  | -improper spacing | -remove two |  | 2 |  |  |
| Quad Teeter Totter |  | -cushioning | -add rubber to bottom of seat | 150 | 2 |  |  |
|  |  | -non sufficient safety zone |  |  |  |  |  |
| PLG04SST - 114W |  | -slide sides | -att 4” width | 400 | 4 |  |  |
| Int. Str. Slide |  | -barriers | -add pickets & egress | 300 | 3 |  |  |
|  |  | -entanglement | -weld | 10 | 2 |  |  |
|  |  | -entrapment | -add backing to stairs | 200 | 3 |  |  |
|  |  | -platform | -add to 22” | 100 | 2 |  |  |
|  |  | -non sufficient safety zone |  |  |  |  |  |
| PLG05GCM - 114W |  | -entrapment | -remove top level |  | 3 |  |  |
| Globe Climber |  | -non sufficient safety zone |  |  |  |  |  |
| Base Material |  | -compact, | -rototill, add base 66T, |  | 8 | 990 |  |
|  |  | -non sufficient | -excavate |  | 8 | 1500 |  |
| Total Cost |  |  |  | 1670 | 49 | 2490 |  |

File Name: K:\PLAY\SCARB\WARD-18\WHTHAV-W.WPD