SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION 		Alisa Craig Parkette		         												Ward 8

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG0101SSW3503P |  | -improper spacing | -remove one baby swing and adjust |  | 3 |  |  |
| Swing Set |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -top beam play surface | -adjust | 15 | 2 |  |  |
| PLG0301JRW3502P |  | -entrapment under slides at support | -fill with stay-white | 200 | 2 |  |  |
| Jr. Cr. Structure |  | -entrapment steering wheel | -change to solid plastic wheel | 100 | 2 |  |  |
|  |  | -log climber & 4X4 climber too wide | -change to rungs | 150 | 14 |  |  |
|  |  | -4X4 play surface | -add 2X2 | 50 | 2 |  |  |
|  |  | -pickets | -add proper access holes | 160 | 10 |  |  |
|  |  | -tire climber in non encroachment zone | -remove |  | 2 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 | 300 |  |
|  |  |  | -excavate |  | 8 | 500 |  |
| Total |  |  |  | 685 | 54 | 800 |  |

File Name: K:\PLAY\NORTH\WARD-8\AILSACR