SITE SPECIFIC RECOMMENDATIONS

EAST 	REGION:	North District

LOCATION		 Chesterie															Ward 17

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM - 150 |  | -improper spacing | -remove two, adjust spacing |  | 1 |  |  |
| 2 Baby, 2 Belt |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -chipped | -paint | 50 | 2 |  |  |
| PLG02SSM - 150 |  | -improper spacing | -remove two, adjust spacing |  | 1 |  |  |
| 6 Belt |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -chipped | -paint | 50 | 2 |  |  |
| PLG03SSP - 150 |  | -not up to standard | -remove and replace | 2000 | 8 |  |  |
| Sr. Spiral Slide |  |  |  |  |  |  |  |
| PLG04CLM - 150 |  | -entrapment | -add backing to stairs | 100 | 4 |  |  |
| Billy Goat Climber |  | -slide width | -add middle | 400 | 3 |  |  |
|  |  | -barriers | -add egress / access | 200 | 3 |  |  |
| PLG05CLM -150 |  | -entrapment | -add pickets | 20 | 1 |  |  |
| Tank Climber |  | -entanglement | -weld skirt | 100 | 2 |  |  |
| PLG06TTM -150 |  | -improper spacing | -remove two, adjust |  | 2 |  |  |
| Quad Teeter Totter |  | -cushion | -add cushion to bottom of seats | 150 | 3 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
|  |  | -non sufficient safety zone | -add base material 66T |  | 8 | 990 |  |
|  |  |  | -excavate |  |  | 1500 |  |
| Total Cost |  |  |  | 3090 | 50 | 2490 |  |

File Name: K:\PLAY\SCARB\WARD-17\CHESTERL.WPD