SITE SPECIFIC RECOMMENDATIONS

SOUTH REGION:	Central District

LOCATION		Lionel Conacher														Ward 23

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM |  | -improper spacing | -remove two, adjust spacing |  | 2 |  |  |
| 4 Belt, 2 Baby |  | -fence in 2Y zone | -relocate swing set 2’ east | 15 | 20 |  |  |
| PLG02SST |  | -entrapment in ladder | -remove and replace | 1000 | 8 |  |  |
| Jr. Str. Slide |  | -small starting section |  |  |  |  |  |
|  |  | -entanglement at top |  |  |  |  |  |
| PLG03INM |  | -tire swing attached | -remove |  | 8 |  |  |
| Sr. Cr. Structure |  | -tube slide has no entrance or exit | -install section | 800 | 16 |  |  |
|  |  | -no barriers | -picket 20’ | 200 | 15 |  |  |
|  |  | -log chain climber has crush pts | -redesign & re-install |  | 4 |  |  |
|  |  | -tire chain climber has pinch pts | -replace with different activity | 1000 | 8 |  |  |
|  |  | -fire pole too close to platform | -re-install |  | 4 |  |  |
|  |  | -pinch pts on all upper body equ | -remove all upper body equipment |  | 24 |  |  |
|  |  | -top of 6X6 posts (play surface) | -cap 10 posts | 100 | 2 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
| TOTAL COST |  |  |  | 3115 | 119 | 0 |  |

File Name: K:\PLAY\SOUTH\WARD-23\CONACHER.WPD