SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	West District

LOCATION 		Falstaff Rainbow Park         												Ward 6

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM2583P |  | -improper spacing | -cut off & replace bearings | 100 | 4 |  |  |
| Swing Set |  |  |  |  |  |  |  |
| PLG02SPR2583P |  | -entrapment between seat and foot rest | -fill with wood | 25 | 1 |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG03SPR2583P |  | -entrapment under handle | -fill with wood | 25 | 1 |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG04SPR2583P |  | -entrapment between handles & body | -install different handles | 200 | 1 |  |  |
| Teeter Totter |  | -entrapment in eye hole | -fill hole with wood | 10 | 1 |  |  |
| PLG05SRW2583P |  | -pinch point on wood chain climber | -retro to under slide of platform | 50 | 3 |  |  |
|  |  | -entrapment between sandbox & platform | -fill with wood | 25 | 1 |  |  |
|  |  | -transition from jr to sr | -picket | 300 | 3 |  |  |
| Base Material |  | -compacted | -rototill, add base 40T |  | 8 | 600 |  |
|  |  |  | -excavation |  | 8 | 1000 |  |
| Total |  |  |  | 735 | 31 | 1600 |  |

File Name: K:\PLAY\NORTH\WARD-6\FALSTAFF