SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION 		Lillian	Park															Ward 10

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM4553P |  | -spacing wrong | -adjust to 30” from boy support |  | 2 |  |  |
| 4 Belt |  | -peeling paint | -repaint | 50 | 2 |  |  |
| PLG02CRC4553P |  | -entrapment | -remove |  | 4 |  |  |
| Rocket Climber |  |  |  |  |  |  |  |
| PLG04SST4553P |  | -barriers - improper entrance | -pickets >30”, enclose entrance | 800 | 10 |  |  |
| Jr. Structure Slide |  | -non sufficient safety zone | -excavate and add base material |  |  |  |  |
| PLG06SSM4553P |  | -too many seats to meet standard | -take out one swing and adjust |  | 2 |  |  |
| 3 Baby |  | -peeling paint | -repaint | 50 | 2 |  |  |
| Base Material |  | -compressed | -rototill |  | 8 |  |  |
|  |  |  | -base material 120 T |  |  | 1800 |  |
|  |  |  | -excavate |  | 8 | 2000 |  |
| Total |  |  |  | 900 | 38 | 3800 |  |

File Name: K:\PLAY\NORTH\WARD-10\LILLIAN