SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	East District

LOCATION		McNicoll Park														Ward 12

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM4560P |  | -S-hooks | -replace | 10 | 1 |  |  |
| 2 Baby 2 Belt |  | -chipped paint | -repaint | 50 | 2 |  |  |
| PLG02SBT4560P |  | -none |  |  |  |  |  |
| Sand Table |  |  |  |  |  |  |  |
| PLG03GRS4560P |  | -barriers | -metal picket heights >30” | 300 | 2 |  |  |
| Billy Goat Climber |  | -rung climbers entrapments | -remove and replace | 600 | 3 |  |  |
|  |  | -entanglement | -modify slide egress | 50 | 2 |  |  |
| PLG04TAT4560P |  | -non sufficient safety zone | -relocate one talk tube | 50 | 8 |  | T.B.D. |
| Talk Tube |  |  |  |  |  |  |  |
| PLG05SSP4560P |  | -barriers | -extend to 38” | 300 | 4 |  |  |
| Int Spiral Slide |  |  |  |  |  |  |  |
| PLG06JRW4560P |  | -barriers | -wood picket >30” egress/access | 100 | 4 |  |  |
| Jr. Structure |  | -undesignated play surface | -replace with 2X6 | 60 | 4 |  |  |
|  |  | -floor boards - nails coming up | -resink and screw | 100 | 6 |  |  |
| PLG07INW4560P |  | -barriers | -wood pickets >30”, egress/ access | 50 | 4 |  |  |
| Int Structure |  | -undesignated play surface | -replace with 2X6 | 60 | 4 |  |  |
|  |  | -entanglements | -2X4 and silicon | 20 | 4 |  |  |
|  |  | -track ride safety zone | -section 14.5 remove and relocate |  |  |  | T.B.D. |
|  |  | -ladder entrapment | -adjust rungs |  | 2 |  |  |
| PLG08SSM4560P |  | -S-hooks | -replace | 10 | 1 |  |  |
| 4 Baby |  | -chipped paint | -repaint | 50 | 2 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
|  |  |  | -base |  |  | 600 |  |
|  |  |  | -excavate |  | 8 | 1000 |  |
| Total |  |  |  | 1810 | 69 | 1600 |  |

File Name: K:\PLAY\NORTH\WARD-12\MCNICOLL