SITE SPECIFIC RECOMMENDATIONS

SOUTH REGION:	Central District

LOCATION		Oriole																Ward 22

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM |  | -improper spacing | -remove one swing, adjust spacing |  | 2 |  |  |
| 3 Belt |  | -too close to timber edge | -relocate swing set | 15 | 15 |  |  |
| PLG02SSM |  | -improper spacing | -remove two swings, adjust spacing |  | 2 |  |  |
| 4 Baby |  |  |  |  |  |  |  |
| PLG03TTM |  | -entrapment in handle | -replace handle |  | 2 |  |  |
| Spring Teeter-Totter |  |  |  |  |  |  |  |
| PLG04SPR |  | -nil |  |  |  |  |  |
| Barber Pole |  |  |  |  |  |  |  |
| PLG05SPR |  | -protrusions on handle & foot rest | -remove and replace | 1200 | 4 |  |  |
| Spring Duck |  |  |  |  |  |  |  |
| PLG06SPR |  | -nil |  |  |  |  |  |
| Spring Koala |  |  |  |  |  |  |  |
| PLG07INM |  | -arch bridge exceeds 48” | -remove & replace | 150 | 25 |  |  |
| Jr. Cr. Structure |  | -no sitting section on slide | -replace slide | 2000 | 8 |  |  |
|  |  | -connected to Sr. with hand climber | -remove climber |  | 3 |  |  |
| PLG08INM |  | -pinch points on tire climber | -replace or redesign | 30 | 12 |  |  |
| Sr. Cr. Structure |  | -fire pole access from two platforms | -picket lower platforms | 10 | 2 |  |  |
|  |  | -6X6 post (play surface) | -cap post (20) | 100 | 5 |  |  |
|  |  | -steering wheel | -replace with solid | 60 | 1 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
| TOTAL COST |  |  |  | 3565 | 89 | 0 |  |

File Name: K:\PLAY\SOUTH\WARD-22\ORIOLE.WPD