SITE SPECIFIC RECOMMENDATIONS

SOUTH REGION:	Central District

LOCATION		Jean Sibelius															Ward 23

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM |  | -improper spacing | -remove one, adjust spacing |  | 1 |  |  |
| 2 Belt, 1 Baby |  | -located in high traffic area | -relocate | 20 | 20 |  |  |
| PLG02SPR |  | -nil |  |  |  |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG03JRM |  | -no barriers | -install pickets ( 8’) | 70 | 6 |  | -total renewal of play space |
| Jr. Cr. Structure |  | -tire swing attached | -remove |  | 6 |  |  |
|  |  | -low slide walls | -remove |  | 2 |  |  |
|  |  | -fireman pole > 60” from platform | -remove |  | 2 |  |  |
|  |  | -entrapment between stairs | -fill with wood | 50 | 2 |  |  |
| PLG04SRM |  | -no barriers | -install pickets (40’) | 350 | 30 |  |  |
| Sr. Cr. Structure |  | -open steering wheel | -replace with solid | 60 | 1 |  |  |
|  |  | -entrapment between stairs | -fill with wood | 40 | 1 |  |  |
|  |  | -tire swing attached | -remove |  | 6 |  |  |
|  |  | -no slide entrance & exit | -replace | 3000 | 6 |  |  |
|  |  | -6 X 6 posts play surface | -install 21 caps | 250 | 4 |  |  |
|  |  | -no slide exit zone | -increase zone | 100 | 15 |  |  |
|  |  | -fireman pole is too wide | -replace | 150 | 4 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
| TOTAL COST |  |  |  | 4090 | 114 | 0 |  |

File Name: K:\SOUTH\WARD-23\SIBELIUS.WPD