SITE SPECIFIC RECOMMENDATIONS

EAST 	REGION:	North District

LOCATION		Snowhill 															Ward 18

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM - 160 |  | -improper spacing | -remove two, adjust spacing |  | 1 |  |  |
| 4 Baby |  | -hanger bearings | -replace | 80 | 2 |  |  |
|  |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -safety zone |  |  |  |  |  |
| PLG02SSM - 160 |  | -S-hooks | -replace | 10 | 1 |  |  |
| 4 Belt |  | -support play area | -cap supports | 150 | 3 |  |  |
|  |  | -safety zone |  |  |  |  |  |
| PLG03TTM - 160 |  | -improper spacing | -remove two, adjust |  | 2 |  |  |
| Quad Teeter Totter |  | -cushioning | -add rubber to seat bottom | 150 | 3 |  |  |
|  |  | -safety zone |  |  |  |  |  |
| PGL04CLM - 160 |  | -barriers | -add pickets to egress | 200 | 3 |  |  |
| Billy Goat Climber |  | -double size slide | -add middle side rail | 400 | 4 |  |  |
|  |  | -safety zone |  |  |  |  |  |
| Base Material |  | -compacted | -rototill, add base material 88T |  | 8 | 1320 |  |
|  |  | -non sufficient safety zone | -excavate |  | 8 | 1500 |  |
| Total Cost |  |  |  | 1000 | 36 | 2820 |  |

File Name: K:\SCARB\WARD-18\SNOWHILL.WPD