SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION 		Tournament Park														Ward 9

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG0101SSM5589P |  | -non sufficient safety zone | -remove timber |  | 4 |  |  |
| 4 Belt Swing Set |  |  |  |  |  |  |  |
| PLG0201SSW5589P |  | -non sufficient safety zone | -excavate and expand |  | 4 |  |  |
| 2 Baby Swing Set |  | -branches | -prune |  | 1 |  |  |
| PLG03CCW5589P |  | -entanglement points all over | -remove or infill | 5 | 4 |  |  |
| Climbing Wall |  |  |  |  |  |  |  |
| PLG0401SST5589P |  | -height/length ratio exceeds .0577 | -remove |  |  |  |  |
| Straight Slide |  |  |  |  |  |  |  |
| PLG0501INW5589P |  | -no pickets on platform | -picket openings over 15” |  |  |  | -replace old structure next |
| Int. Cr. Structure |  | -elevated play surfaces | -cap |  |  |  | to tennis courts |
|  |  | -access components - pickets | -install |  |  |  |  |
|  |  | -slide has entanglement, no exit | -remove and picket |  |  |  |  |
|  |  | -4X4 vertical climbers too wide | -replace with rungs |  |  |  |  |
|  |  | -no head support | -install |  |  |  |  |
|  |  | -entrapment above crawl tube | -remove |  |  |  |  |
|  |  | -remove lower branches from trees | -prune |  |  |  |  |
| PLG06SPR5589P |  | -non sufficient safety zone | -move farther from asphalt |  | 2 |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG07SPR5589P |  | -non sufficient safety zone | -move farther from asphalt |  | 2 |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG08TRM5589P |  | -none |  |  |  |  |  |
| Track Ride |  |  |  |  |  |  |  |
| Teeter Totter |  | -pinch/ crush point, entrapment | -remove and replace |  |  |  |  |
| PLG09SRW5589P |  | -no pickets on platform | -picket openings over 15” |  |  |  | -trees to be removed |
| Sr. Cr. Structure |  | -hand over hand climber spacing | -correct |  |  |  |  |
|  |  | -spiral slide improper for structure | -remove and replace |  |  |  |  |
|  |  | -cable/step climber - improper | -replace |  |  |  |  |
|  |  | -4 X 4 climber | -change to rungs |  |  |  |  |
|  |  | -elevated surfaces, entrapment | -cap |  |  |  |  |
|  |  | -rotted board | -replace |  |  |  |  |
| Base Material |  | -compacted | -rototill |  |  |  |  |
|  |  |  | -base material |  |  |  |  |
|  |  |  | -excavate |  |  |  |  |
| Total |  |  |  | 5 | 17 | 0 |  |

File Name: K:\PLAY\NORTH\WARD-9\TOURNAME